## Slide 1: Evaluation of Rust for Embedded Systems in terms of Security, Performance, and Usability Ankita Kumari ge93vep@mytum.de Advisor: Andreas Finkenzeller Department of Electrical and Computer Engineering Technical University of Munich

## Slide 2: Contents
Introduction and Problem Statement
Security Vulnerabilities
Performance Evaluation
Comparison of Rust with C
Conclusion

## Slide 3: Introduction
The Heartbleed Vulnerability [1]
Example of Buffer overread [2]
C for Embedded Systems

## Slide 4: Motivation
Defense mechanism
  Address Space Layout Randomisation
  Secure Coding
Performance overhead
Garbage Collector
Does not port to assembly
Memory safety
Bad cross-compiling

## Slide 5: Aim
Rust [3]
Evaluate claims of Rust for Embedded Systems
  Security provided by Rust
  Performance of Rust compared to C
  Compatibility of Rust with C libraries (Usability)
Low-level control
Speed
High level
Memory safety

## Slide 6: Introduction to Rust
Suitable for embedded programming:
  Produces predictable assembly
  No garbage collection
Ownership | Every value in Rust has a single owner at a given time
Borrowing | Used to pass the reference but keep the ownership
Mutability | Immutable by default. Makes sharing of data easier. Prevents overwriting
Memory Safety
Type Safety

## Slide 7
Vulnerabilities
Hardware Attack
Software Attacks
Buffer Overflow
Double Free
Invasive Attacks
Non-Invasive Attacks
Vulnerabilities
Hardware Attack
Software Attacks
Invasive Attacks
Use after Free
Side-Channel Attacks
Microprobing
Reverse Engineering
DPA
Security Vulnerabilities in Embedded System

## Slide 8
Rust panics and terminates the program.
let mut a: [char; 2] = ['1', '2'];
let b: [char; 3] = ['1', '2', '3'];
a.copy_from_slice(&b);
let buffer : [u8;30];
let s: [u8;21];
buffer = &s;
Software Attacks - Buffer Overflow

## Slide 9
If payload larger than the buffer input, additional data copied to the output
Payload is upper index of the slice to be copied
Rust panics if tried to access out of bound value from p [1]
let payload:usize = ((input[1] as usize) << 8) + input[2] as usize;
let mut output: [u8;payload+PADDING]; //needs constant size of array
output.extend(input[3..payload].iter().cloned()); //copy of payload string happens here
memcpy(output, input, payload);
Heartbleed Vulnerability in Rust

## Slide 10
1. Dereferencing a dangling pointer
unsafe allows dereferencing the pointer even when it is freed
let p;
{
    let mut x: u8 = 1;
    p = x as *const i32;
}
unsafe{
hprintln!("{}",*p);
}
          Calling functions from other languages
  Bypass the compiler checks
  Interact with hardware
  Access Unions
Unsafe Keyword
Memory Exploits Using Unsafe Keyword

## Slide 11
*big_ptr copy the contents of big_ptr to new_array. Overread by reading the memory past the length of a
let mut a: [u8; 3] = [2,3,20];
let ptr: *mut [u8;3] = &mut a;
let big_ptr: *mut [u8;20] = ptr as *mut [u8;20];
unsafe {
let mut new_array: [u8;20] = *big_ptr;
new_array[10] = 10;
}
let a: [u8; 3] = [2,3,20];
let ptr: *const [u8;3] = &a;
let big_ptr: *mut [u8;20] = ptr as *mut [u8;20];
unsafe {
let mut new_array: &mut [u8;20] = &mut *big_ptr;
new_array[0] = 11;
}
hprintln!("{}",a[0]); \\ prints 11
3. Immutability
2. Overread
Buffer Overread and Immutability

## Slide 12
Vulnerabilities
Hardware Attack
Software Attacks
Buffer Overflow
Double Free
Invasive Attacks
Non-Invasive Attacks
Vulnerabilities
Hardware Attack
Software Attacks
Invasive Attacks
Use after Free
Side-Channel Attacks
Microprobing
Reverse Engineering
DPA
Security Vulnerabilities in Embedded System

## Slide 13
Power analysis of 255 different values of the key position 0 for 1000 traces
Rust
C
No additional safety against the side-channel attacks
Key read out in less than 100 power traces.
Non-Invasive Attacks - DPA

## Slide 14
Vulnerabilities
Hardware Attack
Software Attacks
Buffer Overflow
Double Free
Invasive Attacks
Non-Invasive Attacks
Vulnerabilities
Hardware Attack
Software Attacks
Invasive Attacks
Use after Free
Side-Channel Attacks
Microprobing
Reverse Engineering
DPA
Security Vulnerabilities in Embedded System

## Slide 15
Secure Boolean
  Non-zero values result in True
  255 possibilities to flip a bit
Solution
  Same hamming weight and distance
  Use volatile
enum SecBool {
      SecTrue = 0x9999, \\Hamming Weight(HW)=8 SecFalse = 0x3C3C, \\ HW = 8
      SecInit = 0x5A5A \\ HW = 8
      }
match unsafe { *core::ptr::read_volatile(&val)}
{
SecBool::SecTrue=> hprintln!("TRUE“),
SecBool::SecFalse =>hprintln!("FALSE),
_ => panic!()
};
Secure Coding patterns against Invasive Attacks

## Slide 16
Secure Coding patterns against Invasive Attacks
Secure Return parameter
Secure Branch Handling
Secure Loop

## Slide 17
Optimization Level | O0, O1, O2, O3, Os, Oz
AES algorithm  Used for the performance evaluation
Evaluation is done based on
  Clock Cycles
  NVM Size
  Stack Usage
Performance Evaluation

## Slide 18
Chart: CPU Cycles vs Optimisation levels
| O0 | O1 | O2 | O3 | Os | Oz
Rust | 127516 | 45691 | 3338 | 3774 | 6655 | 8534
C | 15877 | 10562 | 5987 | 5806 | 7071 | 8397
Chart: NVM Size vs Optimisation levels
| O0 | O1 | O2 | O3 | Os | Oz
Rust | 2292 | 918 | 1385 | 1280 | 456 | 492
C | 866 | 428 | 1090 | 1616 | 394 | 348
Evaluation of Clock cycles and NVM Size

## Slide 19
Chart: CPU Cycles with NVM Size
| O2 | O3 | Os
Rust CPU cycles | 3338 | 3774 | 6655
C CPU cycles | 5987 | 5806 | 7071
Rust NVM Size | 1385 | 1280 | 456
C NVM size | 1090 | 1616 | 394
CPU Cycles varying with NVM Size

## Slide 20
Chart: Stack Usage
| O0 | O1 | O2 | O3 | Oz | Os
Rust | 888 | 400 | 136 | 144 | 24 | 24
C | 216 | 128 | 132 | 132 | 112 | 60
Stack Usage

## Slide 21
 | Security |  | Performance |  |  | Usability |  | 
 | Software Attacks | Hardware attacks | Execution Speed | NVM Size | RAM consumption | Inter-portability | Embedded Support | Learning Curve
Rust | ++ | - | ++ | - | ++ | ++ | ++ | -
C | -- | - | + | + | + | ++ | + | ++
Summary

## Slide 22
Performance
Security
Usability
Conclusion

## Slide 23
Analysis of Oz optimization level
Dynamic memory allocation and run-time checks
Using Rust for multi-threaded programming
Future Work

## Slide 24
[1] “The Heartbleed Bug”, https://heartbleed.com/#:~:text=The%20Heartbleed%20Bug%20is%20a,used%20to%.
[2] “Buffer Overread“ https://www.vox.com/2014/6/19/18076318/heartbleed
[3] ‘The Rust Programming Language’. [Online]. Available: https://doc.rustlang.org/book/
[Accessed: 17-Feb-2016].
References

## Slide 25
29.04.2022 | Ankita Kumari | Technical University Munich
Questions?